## Slide 1: UxAS on seL4
John Backes, Rockwell Collins
Dan DaCosta, Rockwell Collins

## Slide 2: What is UxAS?
UxAS: Unmanned Systems Autonomy Services
Collection of software modules that interconnect to automate mission-level decision making
  Task assignment
  Cooperative control
  Sensor steering
Used to conduct experiments and demonstrations of cooperative control and human-machine teaming
Services are deployed across multiple entities

## Slide 3: What would we like to prove about UxAS?
Safety properties
  “Services do not throw exceptions”
  “Services implement their formal specification”
  “The vehicle stays within a safe flight envelope”
  “Multiple vehicles maintain safe separation”
Quality of service properties
  “Messages are processed and delivered in a timely manner”
Security properties
  “Services cannot alter each other’s state except through defined channels”
  “Only trusted commands are executed”
  “Services do not consume resources not allocated to them”

## Slide 4: Problems with initial UxAS
Services/Tasks written in C++
  Not type safe and difficult to reason about formally
Services/Tasks are dispatched sporadically with no bounds on IAT
Framework all runs on Linux (there are bugs)
All Services/Tasks run as threads within the same memory space

## Slide 5: Baseline UxAS Architecture
Fabric: ZeroMQ, CMASI
Line
Point
Zyre: External
Waypoint Manager
Cooperation
Route Planner
Assignment Opt
*
*
Utilities: Timing, Logging, Conversions, *
Area
Overwatch
Persistent ISR
LINUX
All Services/Tasks run in untrusted Linux OS
All Services/Tasks have equal priority and criticality

## Slide 6: Baseline UxAS Architecture
Fabric: ZeroMQ, CMASI
Line
Point
Zyre: External
Waypoint Manager
Cooperation
Route Planner
Assignment Opt
*
*
Utilities: Timing, Logging, Conversions, *
Area
Overwatch
Persistent ISR
LINUX
All Services/Tasks run in untrusted Linux OS
All Services/Tasks have equal priority and criticality

## Slide 7: Possible Solutions to fix UxAS
Change how Services/Tasks are dispatch so system is schedulable
  Middleware group did this
Prove correctness of all UxAS Services/Tasks
  Plausible with significant effort
Prove isolation and correctness of critical tasks so UxAS can meet minimal QoS
  This is what we worked on 

## Slide 8: Key Technologies
The seL4 Microkernel
  Formally verified microkernel maintained by Data61
  Proof is from HOL specification down to the assembly
  Provides formally proven isolation between components
  Can be used as a hypervisor to host guest OS
    Requires specific x86 or ARM instruction sets
Isabelle/HOL and AutoCorres
  Isabelle/HOL is an interactive theorem prover
  AutoCorres is an Isabelle/HOL extension that provides a framework for reasoning about C programs

## Slide 9: Key Technologies
Trusted
Build
Architecture Translation
seL4
eChronos
A
B
C
Assumption: Input < 20
Guarantee: Output < 2*Input
Assumption: Input < 20
Guarantee: Output < Input + 15
Assumption: none
Guarantee: Output = Input1 + Input2
Assumption: Input < 10
Guarantee: Output < 50
Architecture Analysis
Architecture Models
OSATE
Resolute
Assurance Case
AGREE
Behavioral Analysis
SIM
Simulator
Kind/JKind

## Slide 10: UxAS + seL4 Architecture
All Services/Tasks run in untrusted Linux Virtual Machine on top of seL4
Critical services run as isolated native seL4 Services/Tasks
Fabric: ZeroMQ, CMASI
Line
Point
Zyre: External
Cooperation
Route Planner
Assignment Opt
*
*
Utilities: Timing, Logging, Conversions, *
Area
Overwatch
Persistent ISR
LINUX
Waypoint
Manager
Waypiont Manager
seL4

## Slide 11: UxAS + seL4 Architecture
All Services/Tasks run in untrusted Linux Virtual Machine on top of seL4
Critical services run as isolated native seL4 Services/Tasks
Fabric: ZeroMQ, CMASI
Line
Point
Zyre: External
Cooperation
Route Planner
Assignment Opt
*
*
Utilities: Timing, Logging, Conversions, *
Area
Overwatch
Persistent ISR
LINUX
Waypoint
Manager
seL4

## Slide 12: AADL Specification
Component Features
Component
Configuration
Component
Instances
Component
Connections

## Slide 13: Demonstration
Launch attack against UxAS
  Kill UxAS process
  Exhaust all resource in Linux
  Simulates malicious adversary
  Simulates latent bug in UxAS Service
Demonstrate that system still maintains minimal QoS
  The waypoint manager continues to deliver waypoints to the autopilot

## Slide 14: Demonstration
Mission Computer (seL4)
Waypoint
Manager
Asset
Manager
Route
Planner
Linux Virtual Machine
Plan
Assign
Comm
Payload
Serial
Bus
FCC

## Slide 15: Verification of Waypoint Manager
The purpose of the Waypoint Manager is to send subsets of the mission’s waypoints to the flight control computer
“Correctness” means:
  The component never sends more waypoints than the autopilot can handle
  The component sends the next N waypoints whenever the autopilot reaches waypoint N/2

## Slide 16: Arguments for Task/Services and seL4
Argument Purpose:
    Examine ability of UxAS to return home
      Under normal behavior and failure
    Provide rationale/organization for benefits of seL4
Decomposed target UxAS service goal into sub-claims based on architectural components
  Virtual machine (VM) running tasks
  Waypoint manager (WM) running on seL4 kernel with VM
  Connection to Autopilot
  Autopilot running independently
Notes: SeL4: proven mico kernel
Tasks and services running on VM on the micro kernel
Even if VM crashes, WP will get you home

## Slide 17: Future changes to architecture
Fabric: ZeroMQ, CMASI
Line
Point
Zyre: External
Cooperation
Route Planner
Assignment Opt
*
*
Utilities: Timing, Logging, Conversions, *
Area
Overwatch
Persistent ISR
LINUX
Waypoint
Manager
seL4
Task/Service Modeling
Route Planner
Assignment Opt

## Slide 18: What would we like to prove about UxAS?
Safety properties
  “Services do not throw exceptions”
  “Services implement their formal specification”
  “The vehicle stays within a safe flight envelope”
  “Multiple vehicles maintain safe separation”
Quality of service properties
  “Messages are processed and delivered in a timely manner”
Security properties
  “Services cannot alter each other’s state except through defined channels”
  “Only trusted commands are executed”
  “Services do not consume resources not allocated to them”

## Slide 19: Questions?
Find links to project description, code, and other research at:
loonwerks.com